## Slide 1: Data Dump Protocol (DDP)
Presenter: Karthik Shenoy Panambur
Institute: BIBA

## Slide 2
REQUEST
RESPONSE
INITIATE BLOCK TRANSFER
BLOCK TRANSFER - 1
BLOCK TRANSFER - n
.....
.....
ACK
Client
(Mobile)
Server
(Board)
DDP Transaction

## Slide 3
MSG TYPE: REQUEST
MSG TYPE: RESPONSE
Client
Server
Packet type: Transaction packet
  Header
    Transaction ID
    Max Blocks Per Transaction
    Max Packet length
    ACK timeout
Packet type: Transaction type
  Header
    Transaction ID
    Max Blocks Per Transaction
    Max Packet length
    ACK timeout
DDP Request-Response

## Slide 4
MSG TYPE: INITIATE BLOCK TRANSFER
Client
Server
DDP Initiate block transfer
Packet type: Transaction packet

## Slide 5
Server
MSG TYPE: BLOCK TRANSFER
Client
Packet type: Block transfer packet
  Header
    Block metadata
      Frame count
      Continue bit (MSB)
    Data buffer size
  Data buffer
    byte 0 .... n
DDP Block Transfer

## Slide 6
MSG TYPE: ACK
Client
Server
DDP Acknowledgement
Packet type: Transaction packet

## Slide 7
DDP Packet Structure
Transaction Packet
Header
  Msg type : byte 0
  Transaction ID: byte 1-4
  Block per transaction: byte 5
  Max packet length: byte 6
  ACK timeout: byte 7
  CRC: byte 8-9
  Data buffer size: byte 10
Data buffer
  byte 0 ..... n-1 (for data buffer size of n)
Block Transfer Packet
Header
  Msg type : byte 0
  Block metadata: byte 1
    Continue bit: bit 7
    Frame counter: bit 0-6
  CRC: byte 2-3
  Data buffer size: byte 4
Data buffer
  byte 0 ..... n-1 (for data buffer size of n)